## Slide 1
OPENEVOLVE-TUNED L2 CACHE PREFETCH ROUTING
Mixture of Prefetchers
A compact router chooses between MLOP and SPP+PPF after each epoch, then OpenEvolve tunes the policy dictionary.
Final claim size: strong 13-trace training-split validation result, modest heldout generalization over disabled prefetching.
Route the next epoch
Use recent usefulness counters to choose MLOP, SPP+PPF, both, or the off action.
Tune a small policy
OpenEvolve changes budget, score weights, accuracy floor, and tie margin.
Claim the right result size
MoP-V2 reaches 1.066x on 13 training-split validation traces and 1.003x on heldout.
CMU 15-740 class project. Disabled prefetching is the 1.000x reference throughout.

## Slide 2
What we built on Athena
The project adds a router layer and a small policy-search loop above existing Athena L2C prefetchers.
ROUTER NAMES
MoP-V1
Manual one-epoch probe router. It probes both experts, then routes to the higher-scoring expert.
MoP-V2
OpenEvolve-tuned router. It keeps the same public role and tunes budget, scoring, and tie behavior.
Experts
MLOP and SPP+PPF are the two Athena L2-cache prefetchers used by this router.
EVIDENCE LAYER
Epoch-level counters record issued and useful prefetches.
OpenEvolve edits a small literal policy dictionary.
Generated candidate records preserve valid scored rows and fail-closed rows.
Report tables and figures rebuild from simulator summaries.

## Slide 3
Trace protocol and comparators
All performance numbers use disabled prefetching as 1.000x. Best expert is a per-trace reference.
FIXED SETUP
Cache
Athena L2C
Expert pair
MLOP + SPP+PPF
Official split
24 traces total: 17 training, 7 heldout
Final validation
13 available training traces, 500K warmup, 1M simulation
Heldout
7 frozen traces, 20M warmup, 50M simulation
Epoch
500K retired instructions
COMPARISON LADDER
Disabled
Universal 1.000x baseline.
Best expert
max(MLOP, SPP+PPF) per trace, then geomeaned. It is colored dark blue in the result plots.
Worse expert
Minimum practical check for whether routing clears the weaker constituent prefetcher.
Simple routers
WinnerTakeAll, OneShotFit, and Athena MAB appear as small baselines.

## Slide 4
OpenEvolve changed a small policy dictionary
The search could tune router settings and numeric policy weights while the trace split and simulator stayed fixed.
SELECTED MOP-V2 POLICY
Budget
9,216 prefetches per 500K-instruction epoch, about 18.4 per 1K retired instructions
Probe
One initial dual-expert probe epoch
Guardrails
Accuracy floor 30 and 3% close-score tie margin
Weights
Accuracy 1.0, coverage 0.55, traffic 1.0
SELECTION SCORE
Weighted score combines closeness to best expert, IPC over disabled prefetching, margin over the worse expert, tail-loss penalty, and off-action penalty.
Candidate programs received failure scores for simulator failures, unknown policy keys, helper/import code, and missing evolve markers.
Ledger
Rows
All candidates
374
Valid scored
306
Fail-closed
68

## Slide 5
Training-split validation is the main win
Disabled prefetching is 1.000x. Dark blue is best expert, orange is MoP-V1, and pink is MoP-V2.
Caption: The 13-trace validation bars show the main gain from MoP-V1 to MoP-V2. The 7-trace heldout bars show the smaller post-selection result. Prefetcher off is black at 1.000x and best expert is dark blue.

## Slide 6
The numeric result is stronger on training than heldout
Training-split validation carries the quantitative weight. Heldout supports a modest generalization claim.
Surface
MoP-V1
MoP-V2
Best expert
13-trace speedup
1.048x
1.066x
1.085x
13-trace % best
96.5%
98.3%
100.0%
Beats worse expert
9/13
11/13
Below 95% best
3/13
2/13
7-heldout speedup
0.998x
1.003x
1.024x
7-heldout % best
97.6%
97.9%
100.0%
The IPC movement is cycle movement under a fixed retired-instruction window: MoP-V2 has instruction-count ratio 1.000x on both final runs, with cycle-count ratio 0.938x on training-split validation and 0.997x on heldout.
Caption: The routing-behavior plot uses final run summaries to show selected-epoch share, budget share, and useful-prefetch share for MoP-V1 and MoP-V2.

## Slide 7
Heldout behavior is trace-specific
Within each heldout trace the profile order is Expert 1, Expert 2, MoP-V1, MoP-V2. The 1.000x line is disabled prefetching.
Caption: The single experts share one blue hue with different opacity, MoP-V1 is orange, MoP-V2 is pink, and the black vertical line is disabled prefetching at 1.000x.

## Slide 8
The expert pair gives routing something real to choose
MLOP and SPP+PPF have different strengths across traces, so the router has a meaningful selection problem.
Caption: The heldout trace profile shows where MLOP, SPP+PPF, MoP-V1, and MoP-V2 land relative to disabled prefetching at 1.000x.
1.024x
SPP+PPF heldout geomean over disabled prefetching
0.974x
MLOP heldout geomean over disabled prefetching
The best-expert reference is computed per trace, then geomeaned. It is a reference curve for routing quality.

## Slide 9
MoP-V2 clears the simple router baselines
WinnerTakeAll and OneShotFit are intentionally small baselines for the same expert pair.
WinnerTakeAll
Picks the expert with the stronger previous-epoch usefulness score.
OneShotFit
Probes the experts once, then keeps the better early winner.
Athena MAB
Athena's multi-armed-bandit router baseline for the same expert pair.
13-trace method
Speedup
% best
MoP-V2
1.066x
98.3%
WinnerTakeAll
1.025x
94.3%
OneShotFit
1.027x
94.3%
Athena MAB
1.021x
94.2%
Caption: MoP-V2 improves over MoP-V1 on the 13-trace validation set, while the heldout effect is smaller and shown after policy selection.

## Slide 10
OpenEvolve found close candidates across models
Quick-evaluation winners were similar, then wider validation and 13-trace confirmation selected MoP-V2.
Caption: Faint points are quick-evaluation candidates. Dashed lines track the score-selected incumbent IPC, while solid lines track best IPC seen so far.
Model
Iter
Wide val
GPT-5 mini
80
1.087x
GPT-5.4
80
1.088x
Sonnet 4.6
30
1.087x
The selected policy reached 1.089x on the same 10-trace wider-validation set, then 1.066x on the 13-trace training-split validation set.

## Slide 11
Routing behavior remained interpretable
MoP-V2 still acts like a compact epoch router, with observable action choices and budget behavior.
Caption: Final routing behavior stays interpretable: the plot shows how MoP-V1 and MoP-V2 allocate selected epochs, budget, and useful prefetches across the two experts.
The router can choose MLOP, SPP+PPF, both, or the off action after each epoch.
The selected budget and score weights shape these choices without changing simulator internals.
This keeps the final method inside a compact, auditable policy dictionary.
The report keeps raw implementation keys in writing_logistics.md so the main story can use public names.

## Slide 12
Claim and limitations
The final report makes a measured claim: strong training-split validation, small heldout lift, and transparent limits.
CLAIMS
MoP-V2 improves over MoP-V1 on the 13-trace training-split validation set.
MoP-V2 reaches 1.003x over disabled prefetching on seven heldout traces.
Best expert remains a separate reference, with MoP-V2 reaching 97.9% of it on heldout.
Instruction count stays fixed within simulator-rounding error.
LIMITS AND REPRODUCTION
Seven heldout traces make the heldout result a sanity check with visible per-trace variation.
secret_compute_fp_105 remains the largest heldout loss relative to best expert.
Malformed or out-of-contract OpenEvolve candidates stay in the candidate record with failure scores.
Reproduction paths, naming map, and generated-file list live in report/writing_logistics.md.